## Slide 1: DV1C04 Continuous Monitoring in DevOps
L14
Nagios Visualization and Security

## Slide 2: Lessons Overview
Lesson 11: Intro to Continuous Monitoring and Nagios. Download and prep lab. Configure SSH (secure remote execution).
Lesson 12: Install and configure Nagios. Implement local and remote monitoring of servers in a network.
Lesson 13: Configure and implement Nagios monitoring (nagios.cfg, timeperiods, commands, hosts, services, dependencies)
Lesson 14: Automate and customize visualization dashboard. Learn and implement security monitoring.

## Slide 3: Learning Objectives – L14
Utilize Nagios monitoring tool to monitor server health, network, application services, system performance, and event logs.
Demonstrate the Nagios monitoring capabilities.
Apply automation for risks mitigation of applications and infrastructure.
Design customized visualization for Nagios dashboard.
Discover security vulnerabilities using Nagios security plugins.

## Slide 4: Today’s Lesson Flow
Lecture & Demo on Nagios “beneath the hood” configurations.
Demo on Visualization.
Break
Lab on Nagios local monitoring
Lab on Nagios remote monitoring
Debrief
Recap on Nagios security issues.
Sharing on monitoring IT security.

## Slide 5: Nagios Step-by-Step

## Slide 6: Nagios Directory Structure
Main Config File: /usr/local/nagios/etc/nagios.cfg
Log File: /usr/local/nagios/var/nagios.log
Object Config Files: /usr/local/nagios/etc/objects/*.cfg
Nagios Plugins: /usr/local/nagios/libexec // defined in /usr/local/nagios/etc/resource.cfg file
Nagios Web interface: /usr/local/nagios/etc/cgi.cfg
Nagios config file for Apache to interpret: /usr/local/apache/conf.d/nagios.conf
This contains directives for the following URLs:
  http://<nagios-host>/nagios/
  http://<nagios-host>/nagios/cgi-bin/
Nagios Log rotation configuration File: /etc/logrotate.d/nagios

## Slide 7: Nodes and services configuration
Based on templates
This saves lots of time avoiding repetition
Similar to Object Oriented programming
Create default templates with default parameters for a:
generic node
generic service
generic contact

## Slide 8: Generic node template
define host{
name notifications_enabled event_handler_enabled flap_detection_enabled process_perf_data retain_status_information
generic-host
1
1
1
1
1
retain_nonstatus_information 1
check-host-alive
5
60
24x7
d,r nobody 0
check_command max_check_attempts notification_interval notification_period notification_options contact_groups register
}

## Slide 9: Individual node configuration
generic-host switch1 Core_switches 192.168.1.2
router1
switch_group
define host{
use host_name alias address parents
contact_groups
}

## Slide 10: Individual service configuration
define service{
host_name switch1
use generic-service
service_description PING check_command check-host-alive max_check_attempts 5
normal_check_interval 5 notification_options c,r,f contact_groups switch-group
}

## Slide 11: Individual service configuration
define service{
host_name switch1
use generic-service
service_description PING check_command check-host-alive max_check_attempts 5
normal_check_interval 5 notification_options c,r,f contact_groups switch-group
}

## Slide 12: Services
define service{
name service_description is_volatile check_period max_check_attempts normal_check_interval retry_check_interval contact_groups notification_options notification_interval notification_period
ping-service
PING
0
24x7
4
5
1
unix-admins
w,u,c,r
960
24x7
check_ping!100.0,20%!500.0,60%
my-host
1
check_command hosts register
}

## Slide 13: Host and Service Groups
Host and service groups let you group together similar hosts and services:
define
hostgroup{ hostgroup_name alias
}
servicegroup{
4-ServiceNodes
RALPP Service Nodes
define
servicegroup_name
alias
}
topgrid
Top Grid Services
Plus a hostgroups or a servicegroups line in the host or service definition

## Slide 14: Simple Nagios GUI
Ref: https://www.DevOpsSchool.com/
A web interface is used to display the Nagios monitored hosts and services. This is powered by Apache using CGI to generate the dynamic web pages. The symbols on the web page can change to green or red. The output can be sound, graph, etc.
When soft alerts are raised many times, a hard alert is raised. This then triggers the Nagios server to send a notification to the pre-determined administrator.

## Slide 15: Nagios Plugins
Ref: https://www.DevOpsSchool.com/
Nagios Plugins provide low-level intelligence on how to monitor anything and everything with Nagios Core. Plugins operates as standalone applications, but they are designed to be executed by Nagios Core. It connects to Apache that is controlled by CGI to display the results.
Check_nt is a plugin to monitor a windows machine which is mostly available in the monitoring server.
NSClient++ should be installed in every Windows machine that you wants to monitor.
There is an SSL connection between the server and the host which continuously exchange information with each other.
All plugins follow a status code.
The default exit code statuses are:
0 (OK) -The system is working fine;
1 (WARNING) - The system continues to operate but requires attention.
2 (CRITICAL) - The system is not working correctly.
3 (UNKNOWN) - The plugin cannot assess the status of the host or service.
Notes: Nagios Plugins
Plugins are stand-alone add-ons and extensions that allow users to:
- Define targets and parameters on monitored systems.
- Check the state of a host or service.
Plugins are either compiled binaries (written in C, C++, etc.) or executable scripts (Shell, Perl, PHP, etc.) users run from a command line. Plugins run on the Nagios server and enable users to monitor both remote and local hosts via agents or local protocols. Nagios uses the results generated by a plugin to determine:
- The status of the host.
- If the event requires an immediate alert or a simple log on the GUI.
- Whether to run an automatic script for fixing the issue.
Nagios plugins come in three types:
- Official plugins: Nagios develops and maintains around 50 official add-ons.
- Community plugins: There are over 3,000 available third-party plugins developed by community members.
- Custom add-ons: If your team has the right skills, the open-source nature of the tool allows you to create custom plugins.
All plugins follow a status code. The table below explains the default exit code statuses and their descriptions:
EXIT CODE STATUS DESCRIPTION
0 OK The system is working fine.
1 WARNING The system continues to operate but requires attention.
2 CRITICAL The system is not working correctly.
3 UNKNOWN The plugin cannot assess the status of the host or service.
Ref: https://phoenixnap.com/blog/nagios-monitoring-tutorial
===

## Slide 16: Nagios Remote Plugin Executor (NRPE)
Credits: Slide Team Icons and Resources
Nagios Remote Plugin Executor (NRPE) is a Nagios agent that permits the central Nagios server to monitor remote client systems, by executing scripts on the remote hosts and watching for any issue.
It permits for watching of resources like disk usage, system load or the number of users currently logged in at the remote system. This is done through a secure communications channel.
Nagios
Monitoring Server
Remote Host
Command
Result
NRPE
Service
Check NRPF
Check Memory
Check Disk
Check Usage

## Slide 17: Use NPRE to Reduce Firewall Rules
Remote Server Host
Nagios Server
Firewall
Run_remote_checks (using NPRE)
Check_apache
Check_qmail
Remote Server Host
Nagios Server
Firewall
Check Port 80
Check Port 443
Check Port 25
Scenario 2: Nagios uses NPRE remote execution to check if the services are running. One firewall rule required.
Scenario 1: Nagios runs local plugins to check port availability. Three firewall rules required.

## Slide 18: Lab Time

## Slide 19: Nagios SSH Remote Monitoring

## Slide 20: Nagios Plugins
The Nagios package in Ubuntu comes with a number of pre-installed plugins:
apt.cfg breeze.cfg dhcp.cfg disk-smb.cfg disk.cfg dns.cfg
dummy.cfg flexlm.cfg fping.cfg ftp.cfg games.cfg hppjd.cfg
http.cfg ifstatus.cfg ldap.cfg load.cfg mail.cfg mrtg.cfg mysql.cfg
netware.cfg news.cfg nt.cfg ntp.cfg pgsql.cfg ping.cfg
procs.cfg radius.cfg real.cfg rpc-nfs.cfg snmp.cfg ssh.cfg
tcp_udp.cfg telnet.cfg users.cfg vsz.cfg
There are many more available… Just google “nagios plugins”

## Slide 21: Pre-installed plugins in Ubuntu
check_bgpstate check_hpjd check_mailq check_overcr
check_breeze check_http check_mrtg
check_by_ssh check_icmp
check_swap check_ping check_mysql
check_tcp check_pop
check_clamd check_time
check_ifoperstatus check_mysql_query
check_dhcp check_ifstatus
check_udp check_radius check_nntp check_ircd
check_ups check_real check_nntps
check_dig check_users check_rpc
check_disk_smb check_jabber check_nt
check_ssmtp check_pgsql check_mrtgtraf check_ide_smart check_cluster check_procs check_nagios check_imap check_disk check_wave check_sensors
check_dns check_ldap check_ntp check_spop
check_ldaps check_ntp_peer
check_linux_raid check_ntp_time
check_simap check_smtp check_snmp
check_dummy check_file_age check_flexlm
check_load check_nwstat

## Slide 22: Debrief

## Slide 23: Security of Monitoring Systems
Large monitoring systems can become large rootkits!
  Because it needs remote execution rights to the monitored hosts.
  Monolithic agents require privileged system access rights.
  Introduce backdoors / vulnerabilities into otherwise secure systems.
Traditional Monitoring Systems face two main issues:
  Unencrypted channels.
  Privileged root access at the clients.
Rootkit
(privileged root access to monitor system)
Client Node
Monitoring System
Monitoring Server
Unsecured Channel
Man-In-The-Middle (MITM) Attack

## Slide 24: Security Best Practices
Principle of Least Privileges! Off-by-default policy.
UNIX adage: “Do one thing and do it well.”
Nagios: Remote monitoring tasks exist as separate, single-purpose programs that must be configured to be used.
Avoid rexec-style plug-ins that take arbitrary strings and execute them on the remote host (Injection Attacks!).
Communication channel between the remotely executed plug-in and the monitoring system should be encrypted.
Nagios remote execution plugins use industry-standard OpenSSL library.
Use Nagios remote execution service checker to reduce firewall rules.

## Slide 25: SNMP
SNMP = Simple Network Management Protocol
SNMP simplifies device management by enabling centralized discovery, monitoring, and configuration of devices on the network (routers, switches, printers, servers, UPS, IoT devices, and others).
SNMP (v1/v2/v3) vs OID (Object IDentifier) vs MIB (Management Information Base) – refer to notes
SNMP is a mainstay of systems monitoring that is supported on nearly every computing device in existence today.
It is not advised to be used on public networks, and sparingly on private networks because it is susceptible to sensitive data leakage via MITM (Man-In-The-Middle) attacks.
Use SNMPv3 which includes encryption.
Configure as read-only. Only accept connections from specific hosts. Use non-default community string names.
Physically or virtually segregated network (2nd network) as an isolated subnet for SNMP monitoring traffic only.
Ref: PPT Notes
Notes: SNMP is a unique, simple-to-use-and-understand, light-weight Network Management Protocol, UDP based.
There are newer generation protocols like Netflow, and NETCONF; But they add more overheads to do same thing.
===
SNMP simplifies device management by enabling centralized discovery, monitoring, and configuration of devices on the network (routers, switches, printers and others).
It is difficult to find a complete alternative to SNMP because it has been implemented into millions of systems and software over the last 30 years.
If SNMP works for you, then there is no need for an alternative.
===
Question: What is the difference between SNMP v1,v2,v3?
v1 and v2 are authenticated by community. The message is plain.
V3 is more secure, which transfers messages with ciphers. V3 introduced two models: usm and vacm to ensure authentication and authorization security.
Compared with v1, v2 has another function called getbulk.
The version v2 is actually called v2c. What's more, there is another v2u version, which is not used now, and v3 is developed based upon v2u.
===
Question: What is the OID and SNMP?
1: OID = Object Identifier used by SNMP to identify an item used by SNMP to get or set a value, e.g., hostname, memory usage, space available on hard drive, etc.
2: SNMP = Simple Network Management Protocol. Used to query or transmit values (get or set) from a device on a network to another device that is asking for information or attempting to set a value on the target device.
SNMP uses MIB databases identified with OID.
A management information base (MIB) is a database used for managing the entities in a communication network. Most often associated with the Simple Network Management Protocol (SNMP), the term is also used more generically in contexts such as in OSI/ISO Network management model.
Objects in the MIB are defined using a subset of Abstract Syntax Notation One (ASN.1) called "Structure of Management Information Version 2 (SMIv2)" RFC 2578. The software that performs the parsing is a MIB compiler.
The database is hierarchical (tree-structured) and each entry is addressed through an object identifier (OID). Internet documentation RFCs discuss MIBs, notably RFC 1155, "Structure and Identification of Management Information for TCP/IP based internets", and its two companions, RFC 1213, "Management Information Base for Network Management of TCP/IP-based internets", and RFC 1157, "A Simple Network Management Protocol".
Ref: https://en.wikipedia.org/wiki/Management_information_base
===
Question: What is SNMP?
Simple Network Management Protocol (SNMP) is a popular protocol for network management. It is used for collecting information from, and configuring, network devices, such as servers, printers, hubs, switches, and routers on an Internet Protocol (IP) network. Microsoft Windows Server 2003 provides SNMP agent software that works with third-party SNMP management software to monitor the status of managed devices and applications.
Large networks with hundreds or thousands of nodes are difficult to manage without a large staff to monitor every computer. SNMP, which is widely used in local area networks (LANs), lets you monitor network nodes from a management host. You can monitor network devices such as servers, workstations, printers, routers, bridges, and hubs, as well as services such as Dynamic Host Configuration Protocol (DHCP) or Windows Internet Name Service (WINS).
Use SNMP management software to monitor any network device on which you install SNMP agent software. The SNMP agent, which is an optional component of Windows Server 2003, interacts with third-party SNMP management software to enable the sharing of network status information between monitored devices and applications and the SNMP management system that monitors them.
===
One of the most prominent alternative to SNMP is CMIP (https://www.wikiwand.com/en/Common_Management_Information_Protocol) which is still widely used.
CMIP is more powerful in terms of operations supported, hence is more complex.
The main reason SNMP became the front-runner for network management is because of its simplicity (hence the name) compared to other protocols.
Fault management with SNMP works very well due to its simplicity and speed.
===
Question: How will you explain SNMP (Simple Network Management Protocol) to a layman?
I would explain it with a Car Analogy.
You are driving your car (not a vintage one, but a modern one with electronics). You don't see your engine, but you can read how fast you are going via the hand of a gauge on your dashboard, and can also accelerate or decelerate using the accelerator and brake pedals.
Now, imagine if you could change your car's speed by simply turning the hand of the gauge, without using pedals at all. While that's impractical for humans, it's quite logical at the same time: If you turn the hand clockwise, you accelerate to the given speed, and if you turn the hand counter-clockwise, you brake down to the given speed.
That's the principle behind SNMP, which is a network protocol to both gather information (the speed) about network equipment (the engine) in the form of values, and also to change its configuration by telling the equipment to change that same values (the trick with the gauge's hand).
The meaning of many values is standardized, so they can be properly understood independently from the network equipment peculiarities, while the meaning of other values are not (and are meaningful only for that particular brand and model of network equipment).
Many values can just be read (via SNMP get operation), while others can be both read and changed (via SNMP set operations). In many cases, you can also add new values, and after adding them you can change some of them to tell the network equipment to go apply them.
Finally, like a car dashboard where you have indicators lighting up when something special happens, you can be notified by network equipment of peculiar conditions (via SNMP traps).
The interesting thing of SNMP is that reading and changing values is not limited to one piece of network equipment a time, but can also happen for all network devices which are part of a given community. For example, you can send a request to all network devices attached to your network to read a certain value, specifying that only members of a given community (identified by a brief text identifier) should reply with an answer.
SNMP was (and, in the end, still is) popular because:
- quite vendor-neutral (because the meaning of many values are standardized by third-party bodies);
- overall simple (the "S" in "SNMP" stands for simple); and
- does the job at the end of the day.
SNMP is quite old, and there are several versions out there which add some functionalities (for example, SNMPv3 adds encryption). While there are better designed protocols now (like NETCONF), they usually lack a standardization of the values and of their meaning, which greatly reduce their usefulness and advantage over SNMP.
Hope this helps.
===
Question: Why and how do NETCONF and YANG differ from SNMP and MIB?
Initially, SNMP was meant to be used to configure Network appliances. With earlier versions of SNMP (e.g. Version 1 and Version 2) security and reliability was a key issue.
With NFV / SDN appliances, NETCONF, YANG and OpenFlow is now a part of the IT Networking landscape.
NETCONF/YANG provides a standardized way to programmatically update and modify the configuration of a network device. YANG is the modelling language that describes the configuration changes. Whereas NETCONF is the protocol that applies the changes to the Networking Device. The device will maintain the updated configuration.
Terms:
NETCONF = Network Configuration
YANG = Yet Another Next Generation
Ref: https://www.fir3net.com/Networking/Protocols/an-introduction-to-netconf-yang.html
===

## Slide 26: SNMP – A simple explanation (video)
Ref: https://www.youtube.com/watch?v=2IXP0TkwNJU
Notes: https://www.youtube.com/watch?v=2IXP0TkwNJU

## Slide 27: SNMPv3 – Security Breakdown (video)
Ref: https://www.youtube.com/watch?v=NgceiOe9SO0
Notes: https://www.youtube.com/watch?v=NgceiOe9SO0

## Slide 28: SNMP Traps
Ref: https://www.youtube.com/watch?v=RRhp8tQcJyU

## Slide 29: SNMP Traps
Ref: https://www.youtube.com/watch?v=RRhp8tQcJyU

## Slide 30: Nagios Resources
Nagios Home http://www.nagios.org/
Nagios Plugins and Add-Ons Exchange http://www.nagiosexchange.com/
Nagios Tutorial for Debian http://www.debianhelp.co.uk/nagios.htm
Nagios Commercial Support http://www.nagios.com/
Nagios Videos https://www.youtube.com/channel/UCiv97WODwd6sgIgmsy3vqaA
How to Monitor SNMP (Series) https://www.youtube.com/watch?v=oT0tPsrEQgQ&list=PLN-ryIrpC_mAFLgaaA61U0tjH0qV1HP57&index=1
How SNMP Traps Work in Nagios XI network monitor https://www.youtube.com/watch?v=RRhp8tQcJyU

## Slide 31: Thank you