## Slide 1: DV1C04 Continuous Monitoring in DevOps
L13
Nagios Monitoring

## Slide 2: Lessons Overview
Lesson 11: Intro to Continuous Monitoring and Nagios. Download and prep lab. Configure SSH (secure remote execution).
Lesson 12: Install and configure Nagios. Implement local and remote monitoring of servers in a network.
Lesson 13: Configure and implement Nagios monitoring (nagios.cfg, timeperiods, commands, hosts, services, dependencies)
Lesson 14: Automate and customize visualization dashboard. Learn and implement security monitoring.

## Slide 3: Learning Objectives – L13
Describe the mechanics of Nagios monitoring tool.
Utilize Nagios monitoring tool to monitor server health, network, application services, system performance, and event logs.
Demonstrate the Nagios monitoring capabilities.

## Slide 4: Today’s Lesson Flow
Revisit Lab on Nagios installation and configuration.
Demo on Nagios configuration and components.
Break
Lab on Nagios local and remote monitoring
Debrief

## Slide 5: Review & Demo

## Slide 6: Nagios Configuration

## Slide 7: Nagios Configuration Files
Located in /etc/nagios/
Important files:
  cgi.cfg - controls the Web Interface options security
  commands.cfg - commands that Nagios uses to notify
  nagios.cfg - main Nagios configuration file
  conf.d/* - the core of the config files

## Slide 8: Nagios Directory Structure
Main Config File: /usr/local/nagios/etc/nagios.cfg
Log File: /usr/local/nagios/var/nagios.log
Object Config Files: /usr/local/nagios/etc/objects/*.cfg
Nagios Plugins: /usr/local/nagios/libexec // defined in /usr/local/nagios/etc/resource.cfg file
Nagios Web interface: /usr/local/nagios/etc/cgi.cfg
Nagios config file for Apache to interpret: /usr/local/apache/conf.d/nagios.conf
This contains directives for the following URLs:
  http://<nagios-host>/nagios/
  http://<nagios-host>/nagios/cgi-bin/
Nagios Log rotation configuration File: /etc/logrotate.d/nagios

## Slide 9: Lab Time

## Slide 10: Nagios configuration files
Under conf.d/*, files “xxxx_nagios.cfg”:
contacts: users and groups
generic-host: “template” host (default)‏
generic-service: “template” service
hostgroups: host group definitions
services: which services to check
timeperiods: when to check and notify

## Slide 11: Configuration Files
Located in /etc/nagios/
Important files include:
cgi.cfg
Controls the web interface and security options.
The commands that Nagios uses for notifications.
Main configuration file.
All other configuration goes here!
commands.cfg
nagios.cfg
conf.d/*

## Slide 12: Configuration files continued
Under conf.d/* (sample only)
contacts_nagios.cfg
generic-host_nagios.cfg
generic-service_nagios.cfg
hostgroups_nagios.cfg
services_nagios.cfg
timeperiods_nagios.cfg
users and groups default host template default service template groups of nodes
what services to check
when to check and who to notifiy

## Slide 13: Configuration files continued
Under conf.d some other possible configfiles:
host-gateway.cfg
extinfo.cfg
servicegroups.cfig
localhost.cfg
pcs.cfg
switches.cfg
routers.cfg
Default route definition Additional node information Groups of nodes and services Define the Nagios server itself Sample definition of PCs (hosts) Definitions of switches (hosts) Definitions of routers (hosts)

## Slide 14: Pre-installed plugins in Ubuntu
check_bgpstate check_hpjd check_mailq check_overcr
check_breeze check_http check_mrtg
check_by_ssh check_icmp
check_swap check_ping check_mysql
check_tcp check_pop
check_clamd check_time
check_ifoperstatus check_mysql_query
check_dhcp check_ifstatus
check_udp check_radius check_nntp check_ircd
check_ups check_real check_nntps
check_dig check_users check_rpc
check_disk_smb check_jabber check_nt
check_ssmtp check_pgsql check_mrtgtraf check_ide_smart check_cluster check_procs check_nagios check_imap check_disk check_wave check_sensors
check_dns check_ldap check_ntp check_spop
check_ldaps check_ntp_peer
check_linux_raid check_ntp_time
check_simap check_smtp check_snmp
check_dummy check_file_age check_flexlm
check_load check_nwstat

## Slide 15: Nodes and services configuration
Based on templates
This saves lots of time avoiding repetition
Similar to Object Oriented programming
Create default templates with default parameters for a:
generic node
generic service
generic contact

## Slide 16: Generic node template
define host{
name notifications_enabled event_handler_enabled flap_detection_enabled process_perf_data retain_status_information
generic-host
1
1
1
1
1
retain_nonstatus_information 1
check-host-alive
5
60
24x7
d,r nobody 0
check_command max_check_attempts notification_interval notification_period notification_options contact_groups register
}

## Slide 17: Individual node configuration
generic-host switch1 Core_switches 192.168.1.2
router1
switch_group
define host{
use host_name alias address parents
contact_groups
}

## Slide 18: Generic service configuration

## Slide 19: Individual service configuration
define service{
host_name switch1
use generic-service
service_description PING check_command check-host-alive max_check_attempts 5
normal_check_interval 5 notification_options c,r,f contact_groups switch-group
}

## Slide 20: Beeper and sms messages
It's important to integrate Nagios with something available outside of work
  Problems occur after hours... (unfair, but true)
A critical item to remember: an SMS or message system should be independent from your network.
  You can utilize a modem and a telephone line
  Packages like sendpage, qpage or gnokii can help.

## Slide 21: Hosts
define host{
host_name alias address
check_command max_check_attempts check_period notification_interval
notification_period notification_options contact_groups register
}
my-host
my-host.domain.ac.uk 168.192.0.1
check-host-alive 10
24x7
120
24x7
d,r
unix-admins 1

## Slide 22: Services
define service{
name service_description is_volatile check_period max_check_attempts normal_check_interval retry_check_interval contact_groups notification_options notification_interval notification_period
ping-service
PING
0
24x7
4
5
1
unix-admins
w,u,c,r
960
24x7
check_ping!100.0,20%!500.0,60%
my-host
1
check_command hosts register
}

## Slide 23: Command
Commands wrap the check scripts
define command{
check-host-alive
$USER1$/check_ping -H
command_name
command_line
100,100% -p 1
}
and the alerts
define command{
command_name
$HOSTADDRESS$ -w 99,99% -c
notify-by-email
command_line /usr/bin/printf "%b" "***** Nagios *****\n\nNotification
Type: $NOTIFICATIONTYPE$\n\nService: $SERVICEDESC$\nHost: $HOSTALIAS$\nAddress:
$HOSTADDRESS$\nState: $SERVICESTATE$\n\nDate/Time: $LONGDATETIME$\n\nAdditional
Info:\n\n$SERVICEOUTPUT$" | /bin/mail -s "** $NOTIFICATIONTYPE$ alert -
$HOSTALIAS$/$SERVICEDESC$ is $SERVICESTATE$ **" $CONTACTEMAIL$
}

## Slide 24: Check Scripts
The standard nagios-plugins rpm provides over 130 different check scripts, ranging from check_load to check_oracle_instance.p via check_procs, check_mysql, check_mssql, check_real and check_disk
Writing you own check scripts is easy, can be in any language.
Active scripts just need to set the exit status and output a single line of text Passive checks just write a single line to the servers command file

## Slide 25: Contacts
Contacts are the people who receive the alerts:
define contact{
chris Chris Brew 24x7
24x7
w,u,c,r
d,r
notify-by-email
host-notify-by-email someone@somewhere
contact_name
alias service_notification_period host_notification_period service_notification_options host_notification_options service_notification_commands host_notification_commands email
}
Contactgroups group contacts:
define contactgroup{
unix-admins
Unix Administrators
chris
contactgroup_name
alias
members
}

## Slide 26: Time Periods
Time periods define when things, checks or alerts, happen:
define timeperiod{ timeperiod_name | 24x7
alias | 24 Hours A Day, 7 Days A Week
sunday | 00:00-24:00
monday | 00:00-24:00
tuesday | 00:00-24:00
wednesday | 00:00-24:00
thursday | 00:00-24:00
friday | 00:00-24:00
saturday | 00:00-24:00
} | 

## Slide 27: Host and Service Groups
Host and service groups let you group together similar hosts and services:
define
hostgroup{ hostgroup_name alias
}
servicegroup{
4-ServiceNodes
RALPP Service Nodes
define
servicegroup_name
alias
}
topgrid
Top Grid Services
Plus a hostgroups or a servicegroups line in the host or service definition

## Slide 28: Templates
define | host{ use | generic-grid-frontend-host
 | host_name | heplnx201
 | alias address | heplnx201.pp.rl.ac.uk 130.246.47.201
} |  | 
You can define templates to make specifying hosts and services easier:
define host{
generic-unix-host generic-host check-host-alive 10
24x7
120
24x7
d,r
unix-admins
0
name
use
check_command max_check_attempts check_period notification_interval notification_period notification_options contact_groups register
}
Reduces a host definition to:

## Slide 29: Config Files
Main nagios.cfg file can have include statements to pulling other setting files or directories of files
The standard example config files are confusingly spred over several possible files, many of which need
editing to get anything working.
My current set up has the config spread over multiple files and directories.
One set of top level files defining global settings, commands, contact, hostgroups, servicegroups, host- templates, service-templates, time-periods, resources (user variables)
One directory for each host group containing one file defining the services and one defining the hosts

## Slide 30: Debrief

## Slide 31: Thank you